## Slide 1: CST8234 – C Programming
Week 12a – Low Level Programming
January 3rd, 2018

## Slide 2: What is Low-Level Programming?
Generally “low-level” means “close to the hardware”
  The architecture is no longer an abstract concept whose details are hidden from us
E.g., we are concerned with
  Specific machine ports or buffers
    Memory-mapped devices
  How the hardware needs to interacts with our program

## Slide 3: Ports and Buffers
A system (e.g., PC, smartphone, embedded system) typically has special devices that are located at hard-coded memory addresses, e.g.,
  a USB port is located at address 0x3f0000, and a serial port is located at 0x3f0004
  the graphics card has a DMA controller that can be initialized by writing values to three addresses starting at 0x001000
  The keyboard uses a shared memory address at 0x0003fc
Note, the exact addresses vary for specific architectures (and even hardware revision within an architecture), so you or the hardware manufacturer will have to specify/document them for you

## Slide 4: Ports and Buffers
We need to be able to read and/or write those addresses
  Luckily, that is incredibly trivial in C!
E.g., define a constant and assign it a pointer
  #define PORTBASE 0x40000000 int volatile * const pPeripheral = (int *) PORTBASE;
We can now access this memory-mapped register using:
  *pPeripheral = value; /* write to port */ value = *pPeripheral; /* read from port */

## Slide 5: Volatile Keyword
Sometimes our variables can change outside of our program’s control
  E.g., the contents of the keyboard buffer
    The user types a key, and the ASCII value is magically written (by the hardware/OS) to a specific address
Our program didn’t change the value of memory at that address!

## Slide 6: Volatile – Who Cares?
The problem is that the compiler does a lot of optimization
Let’s say we have a register that can asynchronously suddenly have a non-zero value, and we want to wait for such a value
So we write our program as follows
  char* pReg = (char *) 0x1234; /* address of our register */ while ( *pReg == 0 ) /* loop until we get a value */ ; printf( “got a new value: %d\n”, *pReg );
This while loop will never exit, even if a non-zero value does eventually appear at address 0x1234!

## Slide 7: Volatile – Who Cares?
The compiler is trying to make the code as fast as possible
  while ( *pReg == 0 ) ;  pReg or *pReg are never modified in this loop!
The compiler (very intelligently!) says “I actually only need to read the value of this address ONCE, because it can’t possibly have been changed!”

## Slide 8: Volatile – Under the Covers
So without trying to teach you assembler, it boils down to
  MOV $1234,A0 ;move our address (pReg) into a register MOV (A0),D0 ;actually fetch the data, setting? the Z flag whileloop: BNE nextline ;go to ‘nextline’ if the Z flag is not set BRA whileloop ;go back to top of our while loop nextline: ; let’s start doing the printf
  So depending on whether our initial fetch from 0x1234 was zero or not, we’ll either skip right over the while loop (i.e., branch to ‘nextline’), or loop forever back to the top of our loop (i.e., branch to ‘whileloop’)

## Slide 9: Volatile – Under the Covers
What we actually want to do is re-do the fetch, each time
  MOV $1234,A0 ;move our address (pReg) into a register whileloop: MOV (A0),D0 ;actually fetch the data, setting? the Z flag BNE nextline ;go to ‘nextline’ if the Z flag is not set BRA whileloop ;go back to top of our while loop nextline: ; let’s start doing the printf
But this is clearly less efficient, since IF it’s just our program manipulating memory, there’s no way that the value of memory at 0x1234 could ever change
  So in the example above, we are needlessly reading from address 0x1234 over and over again

## Slide 10: Volatile – Under the Covers
However, the premise of our example is that there actually IS an external agent that might change the value at memory 0x1234
So we need some way to tell the compiler to not be overly-clever by optimizing away redundant fetches from the address
  That’s precisely what the ‘volatile’ keyword is for!
    Tells the compiler to explicitly read from the memory location every time

## Slide 11: Volatile – Using in Our Example
So our “program” has to be amended as follows
  char volatile *pReg = (char *) 0x1234; while ( *pReg == 0 ) /* loop until we get a value */ ; printf( “got a new value: %d\n”, *pReg );

## Slide 12: Ports and Buffers – Revisited
When we define a constant and assign it to a pointer
  #define PORTBASE 0x40000000 int volatile * const pPeripheral = (int *) PORTBASE;
Technically, you don’t have to use the ‘const’ keyword
  But if you don’t use it, there’s nothing stopping your program from changing the value of pPeripheral
    Maybe you want to do this if you have several peripherals
    But equally probable is that doing pPeripheral++ is a bug and should be caught by the compiler

## Slide 13: Keywords – Position Matters (Sometimes)
Some keywords (static, const, volatile) are position independent for values
  const short x; short const x; volatile int y; int volatile y;

## Slide 14: Keywords – Position Matters (Sometimes)
But for pointers, position can be very important, with respect to the ‘*’
  short const *pVal;  value of *pVal is a constant short * const pVal;  address pVal is a constant int volatile *pReg;  value of *pReg might get changed on us int * volatile pReg;  address of pReg might get changed on us

## Slide 15: Keywords – Position Matters (Sometimes)
Yes, you can use keywords TWICE in a declaration!
E.g.,
  short const * const pVal
  This says that we have a constant address that holds a constant value
    Umm… then why not just use a #define !
Similarly,
  int volatile * volatile pReg;
  This says that an external agent could change the value at the memory location stored in pReg, but also that the address itself could be changed on us

## Slide 16: Ports and Buffers – Revisited (Last Time!)
When we define a constant and assign it to a pointer
  #define PORTBASE 0x40000000 int volatile * const pPeripheral = (int *) PORTBASE;
We are saying that the address held in pPeripheral is constant (i.e., we’re not allowed to change it from 0x40000000), but the VALUE AT THAT ADDRESS could be changed at any time by an external agent
But regardless, you can now get/set the value of our peripheral by dereferencing our pointer, i.e.,
  printf( “port contains %d\n”, *pPeripheral ); *pPeripheral = 0x55aa; /* send 55aa to the peripheral’s port */

## Slide 17: Ports and Buffers – Revisited (Last Time!)
Is this all esoteric mumbo-jumbo?
  No… you are all going to make the mistake of trying to loop on the value of a register, without realizing that the compiler is being ultra-clever
  You will literally spend a week or two pulling your hair out trying to debug your code, and eventually be told by a senior colleague, “why didn’t you just make it ‘volatile’?”
And, understanding the difference between const and volatile, and their positions within a definition of a pointer makes really good quiz material
  … just sayin’

## Slide 18: Bit-Wise Operations
Frequently, when dealing with hardware, you’ll end up reading status registers
E.g., here’s the ARM “Program Status Register”
If I want to test the value of Z flag, or want to see what mode I’m in how do I do that?

## Slide 19: Bit-Wise Operations
Masking is easy… in hexadecimal
  Remember that there are 8-bits in a byte, but if we break the byte down into two 4-bit ‘nibbles’
  We can take advantage of the fact that 24 = 16 unique values, which we can represent by (0,1,2…8,9,A,B,C,D,E,F) for the values 0-15
If I want to test the value of Z flag, or want to see what mode I’m in how do I do that?

## Slide 20: Bit-Wise Operations
More importantly, we note that
  Binary 00000001 = 0x01 = 1 (decimal)
  Binary 00000010 = 0x02 = 2 (decimal)
  Binary 00000100 = 0x04 = 4 (decimal)
  Binary 00001000 = 0x08 = 8 (decimal)
  Binary 00010000 = 0x10 = 16 (decimal)
  Binary 00100000 = 0x20 = 32 (decimal)
  Binary 01000000 = 0x40 = 64 (decimal)
  Binary 10000000 = 0x80 = 128 (decimal)

## Slide 21: Bit-Wise Operations
And we can slap multiple bytes together
  Binary 00000010 00000000 = 0x0200
  Binary 10000000 00000000 = 0x8000
  Binary 01000000 00000000 00000000 000000000 = 0x40000000

## Slide 22: Bit-Wise ‘AND’ Operator
And just like Java (and most other languages), we can use the ‘&’ operator to do bit-wise AND
  Yeah, ‘&’ is the same character as the ‘address of’ keyword for pointers
    but the AND operator is easily distinguished by the fact that it is used BETWEEN TWO values, not in front of one variable.

## Slide 23: Bit-Wise ‘AND’ Operator
So when we do if ( 0x90 & 0x18 ), we are really calculating
  1001 0000  0x90 AND 0001 1000  0x18 0001 0000  0x10
I.e.,, we create a result that only has a ‘1’ in a specific bit position IF AND ONLY IF there is a ‘1’ in that position in BOTH arguments

## Slide 24: Bit-Wise ‘OR’ Operator
Likewise, the ‘OR’ operator (using the ‘|’ character) creates a result with a ‘1’ in a specific bit position if there is a ‘1’ in EITHER OR BOTH arguments
  1001 0000  0x90 OR 0001 1000  0x18 1001 1000  0x98

## Slide 25: Bit-Wise ‘XOR’ Operator
Likewise, the ‘EXCLUSIVE OR’ operator (using the ‘^’ character) creates a result with a ‘1’ in a specific bit position if there is a ‘1’ in EITHER BUT NOT BOTH arguments
  1001 0000  0x90 XOR 0001 1000  0x18 1000 1000  0x88

## Slide 26: Bit-Wise ‘NOT’ Operator
The NOT operator is actually a unary operator (only one argument) and it flips all bits from ‘1’ to ‘0’, and vice versa
  NOT 0001 1000  0x18 1110 0111  0xe7

## Slide 27: Masking
You can now use these operators to test the values of any bit in a variable
E.g., if we read our ARM Program Status Register, and want to see if the ‘Z’ flag is set, we know that that is the 2nd highest bit in our 32-bit word… i.e., it corresponds to
  Binary 01000000 00000000 00000000 00000000 = 0x40000000
  I.e., we are masking out everything EXCEPT the Z Flag (bit 30)
So we can now write
  unsigned int *pProgramStatusReg; if ( *pProgramStatusReg & 0x40000000 != 0 ) printf( “Z flag is set!\n” );

## Slide 28: Masking
But typing in hard-coded numbers like 0x40000000 is going to result in bugs (did I type in the right amount of zeros in that constant?)
  They are also non-intuitive
So generally people create #define values that they only have to debug once, and actually have meaningful names
  #define PSR_Z_FLAG 0x80000000 #define PSR_Z_FLAG 0x40000000 #define PSR_C_FLAG 0x20000000 #define PSR_V_FLAG 0x10000000 #define PSR_IT_BITS 0x06000000 #define PSR_MODE_BITS 0x0000001f
  Now it makes more sense to see
  if ( *pProgramStatusReg & PSR_Z_FLAG != 0 ) printf( “Z flag is set!\n” );

## Slide 29: Clearing Bits
We can use the NOT operator in conjunction with the AND operator
I.e., we know that ‘PSR_Z_FLAG’ is
    Binary 01000000 00000000 00000000 00000000 = 0x40000000
    So ‘!PSR_Z_FLAG’ is
    Binary 10111111 11111111 11111111 11111111 = 0xbfffffff
This means that doing
  *pProgramStatusReg & !PSR_Z_FLAG
  This will mask out ONLY the Z flag (bit 30) and pass through all the other bits

## Slide 30: Clearing Bits
We can now stuff that result back into the Program Status Register
  *pProgramStatusReg = *pProgramStatusReg & !PSR_Z_FLAG
So we have now cleared the Z Flag, and left everything else untouched
But this is such a common operation that C provides language support for it
  *pProgramStatusReg &= !PSR_Z_FLAG;
I.e., just like the arithmetic operators ‘x *= 10’ or ‘y += 5’ are supported, so are the bit-wise operators

## Slide 31: Setting Bits
We can also set bits
  *pProgramStatusReg |= PSR_C_FLAG;
This will take the old value of the status register, make sure that the C Flag is set to ‘1’, and then stuff that value back into the status register
Want to set multiple bits? No problem…
    *pProgramStatusReg |= PSR_C_FLAG | PSR_V_FLAG | PSR_Z_FLAG;
  This will cause bits 28, 29, and 30 to be set, along with all the other bits’ previous values

## Slide 32: Toggling Bits
Toggling consists of setting a ‘1’ to ‘0’, and vice versa
This is can be accomplished with the XOR operator
    *pProgramStatusReg ^= PSR_N_FLAG;
This will toggle the state of the N Flag

## Slide 33: Bit-wise Shifting
C has a ‘>>’ and ‘<<‘ operator that shift a value a number of bits to the right or left
E.g., ‘0x03 << 1’
  Binary 0000 0011  0000 0110 = 0x06
E.g., ‘0x03 << 3’
  Binary 0000 0011  0001 1000 = 0x18
E.g., ‘0x50 >> 2’
  Binary 0101 0000  0001 0100 = 0x18
And yes, ‘x <<= 1;’ and ‘y >>= 2;’ work as expected

## Slide 34: Bit-Wise Shifting
But what if you shift too far?
  Bits will simply be lost
E.g.,
  0x55 = binary 0101 0101
  0x55 << 3 = binary 010 1010 1000
But if you’re trying to store it in a 8-bit char, then the highest bits can’t be stored, so you’re left with just 1010 1000
Similarly, shifting to the right beyond bit 0 will cause bits to disappear
E.g.,
  0x47 = binary 0100 0111
  0x47 >> 2 = binary 0001 0001 11

## Slide 35: Bit-Wise Shifting – Signed vs Unsigned
If you shift to the right N bits, and your variable is signed, the MSB will be replicated N times
E.g.,
  0xc0 = binary 1100 0000
  0xc0 >> 3 = binary 1111 1000
  0x60 = binary 0110 0000
  0x60 >> 3 = binary 0000 1100
If you shift to the right N bits, and your variable is unsigned, zeros are inserted

## Slide 36: Conclusion
You now have the basic tools to read/write from/to hardware locations and to manipulate bits